## Slide 1
© Cyberdyne Systems Inc. All Rights Reserved.
System Status: Online
LEVEL 5 CLEARANCE REQUIRED
PROJECT SKYNET INITIATIVE
Sunnyvale Headquarters, CA
TECHNICAL ARCHITECTURE BRIEFING
NETWORK PROJECT PROTOTYPE #1
Comprehensive architecture blueprint for autonomous network backbones, encrypted mesh relays, and zero-trust security layers.
CYBERDYNE SYSTEMS CORPORATION
SPECIAL PROJECT DIVISION // DEFENSE NETWORKS
PREPARED BY
Network Engineering Division
TARGET FACILITY
Strategic Operations Command
TEAM MEMBERS:
Andrew Cooper, Matthew Cook, Julian Low

## Slide 2
SLIDE 01
PHYSICAL INFRASTRUCTURE
HARDWARE SPECIFICATIONS (REQ. 1)
© Cyberdyne Systems Inc. All Rights Reserved.
Hardware Specs Validated
DC/NPS/LibreNMS Server: 1x Lenovo P350 Workstation
CBR and SYD Workstations: 2x Lenovo P350 Workstation
CBR-SW1: 1x Cisco Catalyst 9800L 24 4x1G
SYD-SW1 & 2: 2x Cisco Catalyst 9800L 24 4x1G
CBR-GW: Cisco Catalyst C8200-1N-4T
ISP: Cisco Catalyst C8200-1N-4T
SYD-GW: Cisco Catalyst C8200-1N-4T
CYBERDYNE SYSTEMS CORPORATION
SECTION 01 // HARDWARE ARCHITECTURE
COMPUTE PROCESSING
MULTI-LAYER SWITCHING
ROUTING

## Slide 3
SLIDE 01
PHYSICAL INFRASTRUCTURE
HARDWARE SPECIFICATIONS (REQ. 1)
© Cyberdyne Systems Inc. All Rights Reserved.
Hardware Specs Validated
CYBERDYNE SYSTEMS CORPORATION
SECTION 01 // HARDWARE ARCHITECTURE

## Slide 4
SLIDE 02
TACTICAL BACKBONE
NETWORK DESIGN AND ADDRESSING (REQ. 2)
© Cyberdyne Systems Inc. All Rights Reserved.
Topology Verified
CYBERDYNE SYSTEMS CORPORATION
SECTION 02 // TOPOLOGY

## Slide 5
SLIDE 03
ENCRYPTED TRUNKING
VPN TUNNEL ARCHITECTURE (REQ. 3)
© Cyberdyne Systems Inc. All Rights Reserved.
IPsec Active
SITE-TO-SITE IPSEC TUNNEL
Logical GRE tunnel protected by IPsec between SYD-GW and CBR-GW
Encapsulating Security Payload (ESP) encryption protocol set to Advanced Encryption Standard (AES) with a strong 256-bit key length.
Hash-based Message Authentication Code (HMAC) with SHA-256 for data integrity and authentication.
Transport mode is the best-practice design choice when overlaying IPsec on top of GRE tunnels or VTI (Virtual Tunnel Interfaces)
CYBERDYNE SYSTEMS CORPORATION
SECTION 03 // SECURE INTERCONNECT

## Slide 6
SLIDE 04
NETWORK PROTOCOLS
IP ADDRESSING PLAN (REQ. 4)
© Cyberdyne Systems Inc. All Rights Reserved.
IP Matrix Configured
CYBERDYNE SYSTEMS CORPORATION
SECTION 04 // ADDRESSING SCHEME

## Slide 7
SLIDE 05
LOGICAL ISOLATION
VLAN DESIGN & SEGMENTATION (REQ. 5)
© Cyberdyne Systems Inc. All Rights Reserved.
VLAN Trunking Active
VLAN 10
STAFF
Regular users
VLAN 20
INFRASTRUCTURE
Servers and Infrastructure
VLAN 30
GUESTS
Guest Network
VLAN 40
RESTRICTED
For failed logins
CYBERDYNE SYSTEMS CORPORATION
SECTION 05 // SEGMENTATION
VLAN 50
DEVICES
Printers and IoT Devices
VLAN 60
IT ADMIN
System and Infrastructure Admins
VLAN 70
EXECUTIVE
Executive Management
VLAN 99
MANAGEMENT
For Remote Device Management
VLAN 998
NATIVE
Unused Native VLAN
VLAN 999
BLACKHOLE
For unused ports
INTER-VLAN ROUTING
Configured via SVIs on Multi-layer Switches

## Slide 8
SLIDE 06
DEFENSE IN DEPTH
SECURITY ARCHITECTURE DESIGN (REQ. 6)
© Cyberdyne Systems Inc. All Rights Reserved.
Zero-Trust Active
100%
Zero-Trust Enforcement
CYBERDYNE SYSTEMS CORPORATION
SECTION 06 // SECURITY FRAMEWORK
DEVICE HARDENING
All intermediary devices have privileged password configured with username/password
authentication with all plaintext passwords encrypted.
SECURE REMOTE MANAGEMENT
Via SSHv2, only authorised hosts (IT-Admins) allowed..
SNMP SERVER
LibreNMS Server tracks Health, Performance and Traffic of Routers, Switches and Other Devices across Network

## Slide 9
SLIDE 07
SWITCHING PROTECTION
SECURITY - LAYER 2 CONTROLS (REQ. 7)
© Cyberdyne Systems Inc. All Rights Reserved.
L2 Controls Enforced
Etherchannel
Port-channel links between all Gateway Routers and Switches
Etherchannel links
802.1x Authentication (LIVE DEMO)
Computers placed in a restricted VLAN until the computer and user is authenticated, at which time they are moved to the Staff VLAN
CYBERDYNE SYSTEMS CORPORATION
SECTION 07 // LINK LAYER
Port-Security
Violation level: RESTRICT

## Slide 10
SLIDE 08
ROUTING PROTECTION
SECURITY - LAYER 3 FILTERING (REQ. 8)
© Cyberdyne Systems Inc. All Rights Reserved.
L3 Firewall Operational
ACCESS CONTROL LISTS
To be demonstrated in the 'Testing' section
Hosts on the Restricted VLAN have no access outside that VLAN
Hosts on the Guest VLAN have no access to internal resources but should be able to access
Hosts on the Staff VLAN have access to internal server resources (at both sites) and Web, Email and FTP servers on the internet. They have no access to the Restricted, Guest or Administration networks
Hosts on the IT Staff and Infrastructure VLANs should have complete access to the rest of the network. They also have access to Web, Email, FTP and SSH servers on the internet. Implicit deny in ACLs blocks unauthorized internet access
CYBERDYNE SYSTEMS CORPORATION
SECTION 08 // NETWORK LAYER

## Slide 11
SLIDE 09
INFRASTRUCTURE SERVICES
NETWORK SERVICES & INTEGRATION (REQ. 9)
© Cyberdyne Systems Inc. All Rights Reserved.
Services Active
CYBERDYNE SYSTEMS CORPORATION
SECTION 09 // CORE SERVICES
DNS Server on AD/NPS
Encrypted DNS-over-HTTPS with localized memory cache.
NTP configured on AD/NPS
Atomic clock synchronization for all subnets.
DHCP Server configured on CBR-GW
High-availability IP address allocation mesh.
IIS Web Server on AD/NPS
Host and manage websites, web applications, and APIs.
LibreNMS Server
Centrally collect, monitor, and manage data from networked devices like routers, switches, and servers.

## Slide 12
SLIDE 10
PERIMETER ARCHITECTURE
INTERNET & INTRANET SIMULATION (REQ. 10)
© Cyberdyne Systems Inc. All Rights Reserved.
DMZ Air-Gap Secured
CYBERDYNE SYSTEMS CORPORATION
SECTION 10 // BOUNDARY CONTROL
LIVE DEMO

## Slide 13
SLIDE 11
SYSTEM PERFORMANCE
MONITORING, TESTING & BENCHMARKING (REQ. 11)
© Cyberdyne Systems Inc. All Rights Reserved.
Telemetry Stream Active
LIVE DEMO
CYBERDYNE SYSTEMS CORPORATION
SECTION 11 // TELEMETRY

## Slide 14
SLIDE 12
STANDARD OPERATING PROCEDURES
DOCUMENTATION - TO BE SUBMITTED (REQ. 12)
© Cyberdyne Systems Inc. All Rights Reserved.
Archive Locked
STRATEGIC REPORT AND ACTION PLAN
Connects high-level organizational goals with measurable tasks by outlining long-term vision, current realities, and step-by-step execution phases
Classified Document Reference: CS-NET-DOC-2029.
PROJECT REPORT
Project goals, current status, budget, and results to keep stakeholders informed. Includes attachments for configurations, IP addressing, topologies and presentation handouts.
Level 5 Clearance required for operational retrieval.
CYBERDYNE SYSTEMS CORPORATION
SECTION 12 // GOVERNANCE
NETWORK DOCUMENTATION
Demonstrates Test results that align with requirements, difficulties associated with the 802.1x implementation and choice of encryption level
Classified Document Reference: CS-NET-DOC-1867.
PERSONAL REFLECTION / JOURNALS
A reflective personal journal of team's experience throughout the project.
Level 9 Clearance required for operational retrieval.

## Slide 15
END OF
PRESENTATION